## Slide 1: PhD phase  present & future
Chair of Material Science and Nanotechnology
Dipl.-Ing. Steffen Kampmann
02.02.2022 - Zoom
TU Dresden - IfWW

## Slide 2: Multi-scale simulation of functional polymer materials
Functional polymers are used for different kinds of sensors
 e.g. gas sensor, strain sensor
Thin-Films applications
Strain sensors
  Mechanical stability and reliability play a keyrole for many sensing applications
Gas separation membranes
  E.g. Polydimethylsiloxane membranes
[3]
PDMS
[1]
[2]
Multi-scale property description of functional polymers

## Slide 3: End-Crosslinked Polymer Structures
Description:
Generation of end-crosslinked amorphous polymer structures
    Different conversion degrees
Example material
    PDMS (Polydimethylsiloxane)  2 Units (Chain + Linker)
  Deformation & Relaxation of polymer structures
    Strain controlled deformation
    Fitting of common material models (Ogden, Neo-Hook…)
    Determination of mechanical properties
Next step:
Completion and submission of paper

## Slide 4: End-Crosslinked Polymer Structures
Chain
Linker
Chain
Generating structures
  Ca. 40,000 Atoms pro system
  Simulation time: Up to 5 Nanoseconds
     106 timesteps  50 CPU h
It must be ensured that there are enough degrees of freedom for crosslinking
Three different conversion degrees of crosslinking
After crosslinking:
  36 different configurations

## Slide 5: End-Crosslinked Polymer Structures
Strain controlled deformation
Variation of the strain rate, simulation time  Different final strains
Problem:
Raw stress data contents strong fluctuations
Solution:
Matching with different smoothing and filtering methods
Noise reduction is essential for machine learning methods

## Slide 6: End-Crosslinked Polymer Structures
Relaxation at defined strain states of RVE
Use Prony Series to get final value for
Determination of relaxation modulus
Start of relaxation

## Slide 7: Modeling of hyperelasticity based on artificial neural networks
Dipl.-Ing. Lennart Linden
Dr. Karl Kalina
Dr. Jörg Brummund
Prof. Markus Kästner
Collaboration with group of Prof. Kästner
Based on the Ogden material model
We want to substitute the material model based simulation with Molecular Dynamics Simulations
Goal: Prediction of stress-strain-relation
Data mining
Data processing
Training process
[4]

## Slide 8: Modeling of hyperelasticity based on artificial neural networks
Input for the artificial neural network
Fluctuations of strain is negligible
Fluctuations of stress are high
Requirement: MD data must be noise-free
Current step: Waiting for results of artificial neuronal network
 Important to verify different filter and smoothing methods for tensor components

## Slide 9: In situ MD-FEM coupling based on Gaussian Process Regression (GPR)
Based on same idea like ANN
Learning of relation
  Full symmetric tensor description of stress and strain states
Use GPR for in-situ training of stress-strain relation
  Prediction of stress states
Inclusion of molecular dynamics simulations for fitting stress-strain prediction
Current step: Integration of MD-Simulation in 2D

## Slide 10: Conclusion & Overview
tensile and compression tests as data basis to verify structural models
Post-processing of stress data from molecular dynamics simulations
Use of different machine learning methods (ANN, GPR) to describe stress states
[4]

## Slide 11: Literature
[1] https://link.springer.com/article/10.1007/s40843-019-9445-9
[2] Takamatsu et al. ,2010: doi:10.1088/0960-1317/20/7/075017
[3] https://www.businesswire.com/news/home/20150203005027/en/Interstate-Specialty-Products-Supplies-PDMS-Sheets-and-Membranes
[4] Kalina et al., Automated constitutive modeling of isotropic hyperelasticity based on artificial neural networks; Computational Mechanics, 69, pages 213–232 (2022)

## Slide 12: End-Crosslinked Polymer Structures